## Slide 1
Lecture note for Discrete Choice Models
#2
At
Advanced Transportation Planning
Tetsuro HYODO

## Slide 2
Binary Probit Model:
It’s easy to understand Binary Probit model as regression style.
Parameter estimation by maximum log-likelihood is as follows.
 by symmetry of the normal distribution

## Slide 3
Parameter estimation code for Logit & Binary Probit model by R
Data for models: “IZAKAYA happy hour set choice data”
- There are 36 questionnaire sheets, all combination of values are different based on “design of experiments method” (TAGUCHI-method).
Revealed Preference (RP) vs.
Stated Preference (SP)
Q1. After finishing your work, you go to favorite bar. You find the following “happy hour set”. Which one do you prefer ?
Q2. Do you like alcohol drinking ?
1. Yes 2. No
Set-A
Beer 1 glass
Yakitori 2 pieces
Price 300 yen
Set-B
Beer 2 glasses
Yakitori 4 pieces
Price 700 yen

## Slide 4
0,1,1,2,2,6,300,300,0,1
1,0,2,3,2,2,500,700,1,0
0,1,1,3,2,4,300,300,0,1
1,0,1,3,6,2,700,700,0,1
0,1,2,2,4,6,700,300,1,0
0,1,1,3,4,2,500,700,1,0
0,1,2,3,4,4,700,300,1,0
0,1,2,3,4,2,700,700,1,0
1,0,1,2,2,4,300,700,1,0
0,1,2,2,2,6,500,300,1,0
1,0,1,1,2,6,300,700,1,0
0,1,2,3,2,4,500,300,1,0
0,1,1,3,4,4,500,300,1,0
0,1,1,3,6,4,700,300,0,1
1,0,1,3,2,2,300,700,0,1
1,0,2,2,2,4,500,700,0,1
0,1,1,3,4,6,500,500,0,1
0,1,1,2,4,6,500,300,0,1
Students’ answers at the class in 2008 was as follows (CSV file).
1,0,1,1,4,6,500,700,0,1
1,0,1,2,6,2,700,500,0,1
0,1,2,3,2,6,500,500,0,1
1,0,1,2,4,2,500,500,0,1
1,0,2,3,6,4,300,300,0,1
0,1,3,3,2,6,700,500,0,1
0,1,1,2,6,6,700,300,1,0
0,1,2,3,4,6,700,500,1,0
1,0,3,3,4,6,300,500,1,0
1,0,1,2,2,2,300,500,0,1
1,0,1,3,2,6,300,500,0,1
1,0,2,3,6,2,300,700,0,1
1,0,2,3,6,6,300,500,0,1
0,1,3,3,2,4,700,300,0,1
1,0,1,2,4,4,500,700,0,1
0,1,1,1,2,4,300,500,0,1
0,1,1,3,6,6,700,500,0,1
1,0,1,2,6,4,700,700,0,1

## Slide 5
rm(list=ls())
library(maxLik)
setwd("c:/usr/doc/dropbox/daigakuin/beer/")
data <-read.csv("beer2008.csv",header=F)
ns <- nrow(data) ## ns is number of samples
n.alt <- 2 ## number of alternatives
n.var <- 4 ## number of parameters
b0 <- rep(0,n.var) ## set initial parameters
x <- array(0,c(ns,n.alt,n.var)) ## make independent variable matrix
y <- array(0,c(ns,n.alt)) ## make choice result matrix
## set matrix of variables
x[,1,1] <- data[,3]; x[,2,1] <- data[,4]
x[,1,2] <- data[,5]; x[,2,2] <- data[,6]
x[,1,3] <- data[,7]; x[,2,3] <- data[,8]
x[,1,4] <- 1
y <- data[,1:2]
R code: Logit_maxLik.r

## Slide 6
## Log-Likelihood function of Logit Model
logit <- function(b) {
u <- matrix(0, nr=ns, nc=n.alt) ## utility function
p <- matrix(0, nr=ns, nc=n.alt) ## probability
for(i in 1:n.alt) u[,i] <- exp(x[,i,] %*% b)
for(i in 1:n.alt) p[,i] <- u[,i]/rowSums(u)
a <- p*y; prb <- rowSums(a)
LL <- sum(log(prb))
return(LL)
}
## Log-Likelihood function of BinaryProbit Model
probit <- function(b) {
u <- matrix(0, nr=ns, nc=n.alt)
p <- matrix(0, nr=ns, nc=n.alt)
for(i in 1:n.alt) u[,i] <- x[,i,] %*% b
p[,1] <- pnorm((u[,1]-u[,2]), mean=0, sd=1)
p[,2] <- 1-p[,1]
a <- p*y; prb <- rowSums(a)
LL <- sum(log(prb))
return(LL)
}

## Slide 7
## Maximization of Log-Likelihood by “maxLik"
res <- maxLik(logit,start=rep(0,n.var))
# res <- maxLik(probit,start=rep(0,n.var))
## estimated parameter & Hessian
b <- res$estimate; hhh<-res$hessian
## estimating t-value
tval <- b/sqrt(-diag(solve(hhh)))
## Initial Log-likelihood
L0 <- ns*log(1/n.alt)
## Final Log-Likelihood
LL <- res$maximum
## Goodness of Fit
## rho-square
print((L0-LL)/L0)
## rho-square adjusted by degree of freedom
print((L0-(LL-length(b)))/L0)
print(b); print(tval)

## Slide 8
The estimated parameters by Logit model:
rho: 0.5718, rho-bar: 0.4115
parameters:
0.717 0.573 -0.0109 0.632
t-values:
0.827 2.34 -2.87 0.567
Vset-A= 0.717Beerset-A +0.573YAKITORIset-A -0.0109priceset-A +0.632
Vset-B= 0.717Beerset-B +0.573YAKITORIset-B -0.0109priceset-B
The estimated parameters by Probit model:
rho: 0.5768, rho-bar: 0.4165
parameters:
0.506 0.333 -0.00625 0.442
t-values:
1.13 2.51 -3.28 0.742

## Slide 9
Vset-A= 0.717Beerset-A +0.573YAKITORIset-A -0.0109priceset-A +0.632
Vset-B= 0.717Beerset-B +0.573YAKITORIset-B -0.0109priceset-B
By using this result, we can evaluate the relative value among two variables.
This equation means “Beer ” is equivalent to “one YAKITORI”. From the above equation, we can calibrate , so one YAKITORI equals 0.8 Beer.
one Beer’s monetary value is 66 [yen/Beer]
V = - 0.04time[min.] - 0.0015cost[yen]
[yen/min.]
This is called “Value of Time” (VOT). Very important value for transportation planning, especially evaluating “Benefit”.

## Slide 10
Several type of variables:
Typical example of urban modal choice
R:rail, B:bus, C:car
-Common variable: time, cost…
-Alternative specific variable: # of transfer, # of cars, driving license dummy…
-Social Economics variable: age, gender, income…
-Intercept: maximum number is “# of alternatives – 1” why ?

## Slide 11
An example shown in “Discrete Choice Methods with Simulation” by K.Train (2009)

## Slide 12
Discrete Choice Modeling by R & Biogeme
R: homemade (MNL, NL, MXL), mlogit, MNP
Biogeme: MNL, NL, MXL, Taste Variation, CNL
using 5 alternatives & 1,000 samples
Intercity freight data
May, 2018
Tetsuro HYODO
hyodo@kaiyodai.ac.jp

## Slide 13
日本語による前文
2009年1月に，自身のHP上で，「Rによる離散選択モデルの推定方法メモ」
http://www2.kaiyodai.ac.jp/~hyodo/Logit_by_R.pdf
を公開し，ありがたくも何名かの方から，「役に立っています」とのお言葉を頂いた．
しかし，さすがに9年が経過し，色々と不具合も目立ってきた．申し訳ないのだが，最大の問題は，最尤推定に “optim” を使用していたことで，これは特に選択肢の利用可能性がマチマチな時に正しいパラメータを導いてくれないことが判明していた．maxLikを用いれば，現時点では問題がないことが分かっている．あとはNLの記述が，現在GEV由来が主流であることか．GEV式の方が自家製コードも楽に作ることができる．
さて，2017年度の卒論で，本州－北海道間の物流センサスを用いた5経路の輸送手段選択モデルに取り組んでいた．実はこのデータが，様々な離散選択モデルのテストデータとして優れており，担当卒論生や博士課程の留学生も交えて，バリエーション多彩なモデル群を試すことになった．
そして，2018年度前期，大学院の授業で非漢字圏の修士学生を対象に，3年ぶりに英語授業をすることになった．そこで，この際，卒論で手がけた一連のモデルを，ある一つのデータ（卒論データから抽出した1,000サンプルデータ）への適用コードとして（怪しい）英語で整理することを試みた．Rによる自家製コード，mlogit，Biogeme，MNP がその構成要素である．自習可能なように，コードやデータも同梱しました．適宜，試してみて下さい．
種々のコード作成にご協力頂いた，佐々木葵さん（修士1年），Seiji LIDASAN君（博士2年）に感謝申し上げます．

## Slide 14
Tomakomai
Hachinohe
Aomori
Hakodate
Ibaraki
Tokyo
Hokkaido
1.IbarakiTomakomai
2.TokyoTomakomai
3.KantoHachinoheTomakomai
4.KantoHokkaido (rail)
5.KantoAomoriHakodate
Kanto
Data is freight modal choice between Kanto & Hokkaido

## Slide 15
1.ibaraki
2.tokyo
3.hachinohe
4.rail
5.seikan
Time [hour]
Cost [1,000yen]
Time & cost relationship
(10ton cargo is assumed)
By NITAS ver. 2.4

## Slide 16
Data structure:
One sample (1 row)
from the data is transposed
for easy viewing.
2 common variables (time and cost), 1 socioeconomic(SE) variable (log10(weight)).
Another variable type is “alternative specific”,
what is this variable?
“goods” is goods type, but is not used in this case.
d1000.csv

## Slide 17
Estimation of Multinomial Logit (MNL):
-Don’t use “optim”
-”maxLik” is better
-”with gradient function”,
it is faster
-”rowSums” is 40% faster than “apply(x,1,sum)”  why ?
MNL.r

## Slide 18
L(0)= -1359.237 initial log-likelihood
L(*)= -1112.049 final log-likelihood
rho= 0.1818578 rho-bar= 0.1745007 log-likelihood ratio
1 , -0.017264 , -1.64 time [hour], t-value
2 , -0.01694384 , -8.19 cost[1000yen]
3 , 0.4128331 , 3.94 log(weight.ton)-1.ibaraki
4 , 0.0756141 , 0.65 log(weight.ton)-2.tokyo
5 , -0.8467355 , -8.27 log(weight.ton)-3.hachinohe
6 , 0.6351293 , 5.13 log(weight.ton)-4.rail
7 , 0.5342334 , 1.63 intercept-2.tokyo
8 , 2.652349 , 11.08 intercept-3.hachinohe
9 , -3.677233 , -7.52 intercept-4.rail
10 , 0.4521059 , 1.53 intercept-5.seikan
Hit ratio(%): 40.575
1 2 3 4 5 total
1 122 2 72 3 1 200
2 48 0 52 0 0 100
3 26 3 463 0 8 500
4 70 0 26 4 0 100
5 19 0 42 5 34 100
Total 285 5 655 12 43 1000